## Slide 1: Blaine Sewer Capacity Review: East of I-5
Bernie Ziemianek and Greg Burg, Public Works
Rodney Langer David Evans and Associates, Inc.

## Slide 2: Sewer System East of I-5
Several sewer basins
Three “trunk” lines converge between G St and H St in one sewer main crossing under I-5
Other I-5 crossings to north

## Slide 3: 2005 General Sewer Plan (GSP)
Flow Data Collection
Population Growth – 20 years
  4,100 to 10,900 persons
  75% of growth east of I-5
Hydraulic Model
  25-yr, 24-hour event
  predict level of flow in pipes
Condition Assessment Recommended – need info
Projects recommended (not including I-5 crossing):
  6,620 LF
  $3.7 million (2020 $)
Prior to new treatment facility

## Slide 4: Capacity and Surcharging
Gravity Flow
  Max. capacity at full pipe
  Function of pipe slope
Pressure Flow
  Flow > Gravity capacity
  “Surcharging”
  Increased capacity but water level above pipe
  Filling manholes
  Backup in side-sewers
  Impacts capacity upstream
Ground Level
Sewer Main
Surcharging Level
Manhole

## Slide 5: Surcharging
Anticipated
  I-5 Crossing and upstream in Trunk H4 and Trunk H5
  Surcharge to ground west of schools complex
Observed
  Two locations west/southwest of schools complex

## Slide 6: Focused Upgrades
Schematic Model
  Interpret results of 2005 GSP
  Data gaps/discrepancies
Defer Work Across I-5
  Time, Permitting and Cost
  Optimal long-term solution?
Upgrade Next Four Pipes
  Reduce Surcharging Impact
  Eliminate impact upstream in Trunk H5

## Slide 7: Action Plan
Sewer System Mapping
  For design, future hydraulic model and updates in GIS
CCTV/Manhole Inspections
  Bellies/Roots/Sediment?
Sewer Main Improvements
GSP Update
Future Improvements

## Slide 8: Trunk H5 Condition
Total Length – 3,300’ +/-
> 50% PVC, slope deficiencies
Multiple significant bellies
A few structural defects
Preliminary Recommendation
  12” – 2,500 feet +/-
1
2
3
4
5/6
7

## Slide 9: Recommended Improvements
Replace near I-5 (10” to 24”)
New trunk in G St. (18” & 15”)
Replace near SR 543 (8” to 15”)
Replace in 8th St. (8” to 12”)
Replace Trunk H5 (8” to 12”)
Replace lateral (6” to 8”)
6,800 feet +/-
$5 million project cost (preliminary)
8
2
3
4
5
1
6

## Slide 10: System Capacity
Actual growth through 2020 about 60% of forecast City-wide
WITHOUT IMPROVEMENTS
  Capacity deficiency – original projects planned for completion by 2009
  Condition deficiency – structural and capacity-limiting conditions found, additional areas to investigate
WITH RECOMMENDED IMPROVEMENTS
  Catch-up with core set of improvements recommended in 2005 for future growth
  Add additional capacity in anticipation of growth not previously forecast
  Address significant condition deficiencies in Trunk H5 and increase capacity for airport development area

## Slide 11: System Benefits
Targeted projects to increase capacity and remove structural deficiencies
Catch-up with 2005 GSP Recommended Improvements for 20-year forecast population
Allow time for more detailed analysis
  New GSP - Future Projects:
    I-5 Crossing upgrade or additional crossing
    Other capacity or condition solutions